## Slide 1
ATM Asynchronous Transfer Mode at the Data Link Layer
By : Raghav Panthi

## Slide 2
ATM's Core Function at Layer 2
ATM stands for Asynchronous Transfer Mode.
It is a high-speed networking technology used
to transfer data, voice, and video over a network.

## Slide 3
Role of Atm
1
Framing
Organizing data into distinct frames (cells) for transmission.
2
Error Detection
transmission errors are find out .
3
Flow Control
Managing data transmission rates between devices to prevent overflow.
4
Reliable Transfer
Ensuring accurate and ordered data delivery between connected devices.
ATM excels in these responsibilities by systematically breaking down data into small, manageable, fixed-size units known as "cells."

## Slide 4
ATM Structure
Central to ATM is its cell-based architecture Each ATM cell consists of 53 bytes, divided into two main parts:
Header
5 bytes
Contains addressing and control information(error checking bit).
Payload (Data)
48 bytes
Carries the actual user data.

## Slide 5
Why the Fixed Cell Size?
Faster Processing
Predictable cell size allows for streamlined hardware processing.
Low Delay
Reduces latency, making it ideal for real-time applications.
Converged Traffic
Optimized for integrating voice, video, and data efficiently.
This design choice is critical for ATM's ability to handle diverse traffic types with consistent performance.

## Slide 6
Working of ATM
Large data is divided into small cells (53 bytes)
Each cell is sent through a predefined path.
Virtual circuit.
Cells traverse the network sequentially
At the destination, cells are precisely reassembled into their original data streams.
Photo ,video

## Slide 7
ATM _ Virtual Circuits
ATM uses connection-oriented communication
A fixed path is created before data transmission starts.
This fixed path is called a Virtual Circuit.
Virtual Path (VP):
Virtual Channel (VC):
The actual path used by ATM cells
Carries one stream of data
one channels has only one type of data either (voice, video, or text)
Acts like a car/buses etc to transfer data
A group of Virtual Channels
Acts like a main road for frame.
➡ Once VP and VC are established, data flows continuously, quickly, and in order.

## Slide 8
Key Features of ATM at Data Link Layer
Fixed Cell Size
Standardized 53-byte cells ensure consistent performance.
Connection-Oriented
Establishes a virtual circuit before data transmission begins.
High Speed
Designed for high-bandwidth broadband networks.
Supports QoS ( Quality of Service)
Allows for differentiated service and prioritization of various traffic types.

## Slide 9
9. Applications of ATM
ATM was used in:
1. Telephone Networks
📞 Used for: Voice calls
audio data
2. Broadband Services
🌐 Used for: Internet access
Text data ,Image data
Video Conferencing
🎥 Used for: Online meetings and video calls
4. Early Internet Backbone Networks
🌍 Used for: Main internet connections between
countries
Multimedia (text, audio, video, images).